## Slide 1
Slave Unit
Valve
Slave Unit
Valve
Slave Unit
Valve
Slave Unit
Valve
Slave Unit
Valve
Master Unit
Slave Unit: Customized LoRaWAN board for valve control
Master Unit: LoRa Gateway integrated with BLE for UI
Single Site

## Slide 2
Master Unit Block Diagram
LoRa Module
Semtech SX1262
PhyTec SBC
BLE Module for UI
I/O interface Module for wired inputs
LoRa Module to wirelessly switch ON/OFF Slave Units
SBC to communicate with all modules for control and UI
BLE Module to provide the User-defined inputs to the system
4G SIM Based Network adapter for implementing MQTT services and pushing the data in the Application layer
4G SIM based Network adapter
Internet
MQTT Subscribe and Publish

## Slide 3
I/O Considerations
Wired Inputs
1. Mains on and off
2. Check compressor power available
3. Check pump power available
4. Compressor pressure sensor
5. Wind sensor
6. Dust sensor
7. Irradiation sensor
8. Rain sensor
9. If Possible (inputs from solar inverters that connect
through RMS, remote monitoring system)
BLE (Bluetooth inputs)
1. Mode selection (5 modes)
2. No of daily cycles of operation
3. Day timmings of each cycle of operation
4. Duration of air flow = 5 seconds to 30 seconds
5. Duration of water flow= 10 seconds to 120 seconds
6. Wait period for compressor to become full, 1 minute to 10 minutes
7. Duration of soap discharge from 5 seconds to 30 seconds
Wired outputs
1. Compressor On
2. Water pump On (Through a single phase or 3 phase contactor)
3. 6 valves On

## Slide 4
internet
Peripheral
8-channels
Peripheral
8-channels
Peripheral
SBC
RS 232
2 ports
RS 485
1 port
*RS485- MODBUS
*RS232-UART
Micro Bus
LTE SIM Module
*MPCI-4G modem
*MICRO USB
Wired Inputs :9, if needed go for Arduino Mega
1. Mains on and off
2. Check compressor power available
3. Check pump power available
4. Compressor pressure sensor
5. Wind sensor
6. Dust sensor
7. Irradiation sensor
8. Rain sensor
9. If Possible (inputs from solar inverters that connect
through RMS, remote monitoring system)
Wired outputs : 8
1. Compressor On
2. Water pump On (Through a single phase or 3 phase contactor)
3. 6 valves On
Arduino Nano
Semtech Transceiver
Waveshare Industrial Modbus RTU 8-Channel Relay
**AT Commands/MRAA library
**SW::LibModbus
**SW::LibModbus
*Microbus BLE
**paho MQTT3
BLE Link
**SW: BlueZ 5.50
BLE (Bluetooth inputs)
1. Mode selection (5 modes)
2. No of daily cycles of operation
3. Day timmings of each cycle of operation
4. Duration of air flow = 5 seconds to 30 seconds
5. Duration of water flow= 10 seconds to 120 seconds
6. Wait period for compressor to become full, 1 minute to 10 minutes
7. Duration of soap discharge from 5 seconds to 30 seconds
AC to DC adapter >15 W
Notes: When the rain has started and stopped
Intensity
Integrated humidity
Dust level on the solar panel

## Slide 5
LoRa Node: Connected to Valve
HL KPM 05

## Slide 6
Item Desciption | Qty | Unit List Price (₹)
Waveshare Industrial Modbus RTU 8-Channel Relay Module RS485 Bus, Multi Protection | 1 | 3,180
Semtech SX1280 Long range, low power 2.4 GHz Wireless RF Transceiver with ranging capability | 1 | 1200 (Have asked semtech for price)
ARDUINO NANO | 1 | 1500
Multi-Protocol IoT Gateway - A5D2x 512 MB RAM | 1 | 12500

## Slide 9
L=12 inch
W=7 inch
H=7 inch

## Slide 10
OD 21mm
ID 15 mm

## Slide 11
Application Framework
Test Module
Communication Module
Mode/Cycle Module
Digital Interfacing Module
LoRa Link Test
RTC Clock Test
Interface Test
LoRa P2P
MQTT Service
Wifi Broadcasting for mobile HMI
Time-Slotted Actuation
User Control
Modbus
UART